## Slide 1: Weekly Report
2026/08/10 Amir Fathi

## Slide 2: Highlights
Highlights of this week:
  iSCAT-Confocal colocalization for 50% BMP with DOPE-Biotin and DOPE-Cy5 (unsuccessful)
  Prepared new batch of SUV for 25% BMP with DOPE-Biotin and DOPE-Cy5 markers
  Single molecule emitter validation
Next:
  Validate the single molecule emitter for other data sets with multistep fitting.
  Do SPT with iSCAT for BMP 25% + TAT
  As in domains show more confinement, find a way to quantify the confinement using gyration tensor, ergodicity analysis, transient confinement analysis, and other metrics
  Do more experiments for phase separation
  Find a way to calibrate confocal image with the iSCAT image
  More simulation for the random phase mask to find the optimal parameters for the diffuser

## Slide 3: 50% BMP with DOPE-Biotin and DOPE-Cy5
I prepared two SLB samples. In both sample I can see the membrane (not its fluidity) in the confocal image (DOPE-Cy5 channel). However, When I switch to iSCAT acquisition, I can only see stationary GNPs (not undergoing Brownian motion). I tried different regions of the sample, but I couldn’t find any mobile GNPs. Therefore, I prepared a new batch of SUV for 25% BMP with DOPE-Biotin and DOPE-Cy5 markers which has a better chance of success when preparing the SLB sample.

## Slide 4: Single Molecule Emitter Validation (Single Step Fitting)
The histogram shows a unimodal distribution, it is likely that the signal is from a single molecule. In the figure above, the histogram show single-emitter step size (ΔI) 306±158. a.u. Here, I filtered more than 7000 trajectories and found 167 trajectories that shows clear signal drops. I have tested this on sample with TAT-B with 25% BMP. Please note that the analysis was done on the sum of all pixels designated to a particle that trackpy reports.
Metric | Value
Total trajectories in dataset | 7,747
Trajectories ≥ 15 frames analyzed | 7,747
Qualifying single-step bleach events | 163 (2.1% of analyzed)
Average single-molecule step size (ΔI) | 306.98 ± 158.53
Average background noise level (σ) | 56.86 ± 39.64
Average Step Signal-to-Noise Ratio | 7.06

## Slide 5: Single Molecule Emitter Validation (Multistep Fitting)
Although the histogram when only searching for single-step bleach events shows a unimodal distribution, when I can find many trajectories that show multiple bleach events.
Total trajectories in dataset: 7747 Trajectories >= 15 frames analyzed: 7747 Qualifying stepwise bleaching tracks: 187 (2.4% of analyzed) 1-step class (Monomer): 89 tracks (47.6%) 2-step class (Dimer): 88 tracks (47.1%) 3-step class (Trimer/Aggregate): 7 tracks (3.7%) 4-step class (Trimer/Aggregate): 2 tracks (1.1%) 5-step class (Trimer/Aggregate): 1 tracks (0.5%)

## Slide 6: Single Molecule Emitter Validation (Histogram)
I also tried to plot the histogram of the signal intensity for all trajectories at different time points. The histogram shows a unimodal distribution, but they could be from multiple emitters. Therefore, I think the multistep fitting is a better way to validate the single molecule emitter.

## Slide 7: Inline and display math
This is inline math: mv² + α × β³, embedded right in a sentence.
Note: pandoc’s PPTX writer starts a new slide after an image, so put display math at the end of a slide — one display equation per slide.
Subscript and Superscript: x₁² + x₂² = x₃².
A display equation (kept as the last block of this slide):

## Slide 8: Meeting Summary
Paul
The fitting for TAT affinity is improved for better fitting and better visualization.
Time dependent images for SPT analysis is done for 0, 1, 2, 3, 4 and 5 hours after TAT addition.
Tony
…
Peggy
Based on the concentration dependence of LNPs the next round of experiments will be done with 10x higher concentration.
Andrew
Temperature dependent experiment shows that domains formed after TAT addition disappear at 50 °C. However, when the sample is cooled down to room temperature, the domains do not reappear.
Next is to analyze the SPT for DOPE-Atto488 and Cholesterol-Bodipy to see if the diffusion coefficient is different for the two markers.